## Slide 1
PLANT DESIGN AND LAYOUT
MANUFACTURING OF ACETONE
SUBMITTED TO:-
DR. SACHIN MANDAVGANE (PROFESSOR)
DEPT. OF CHEMICAL ENGINEERING
VISVESWARAYA NATIONAL INSTITUTE OF TECHNOLOGY, NAGPUR

## Slide 2
OUR TEAM
ANSHUL LOKHANDE(BT23CME010)
CHAITANYA TALE(BT23CME016)
ATHARVA JOSHI(BT23CME025)
VIVEK KUMAR(BT23CME027)
ASHISH KUMAR(BT23CME109)
KAUSTUBH MAHAJAN(BT23CME093)
SAURABH CHAVAN(BT23CME105)
PRIYAM (BT23CME096)
VISHAL PATIL(BT23CME106)
SOHAM KARVE(BT23CME091)
AMIT PATRA(BT23CME085)
VEDANT ROKADE(BT23CME015)
ROHAN SWAIN(BT23CME020)

## Slide 3
  We are deeply honored to have had the opportunity to design a storage vessel and a plant for manufacturing acetone from cumene, derived from propylene and benzene, gaining valuable insights into industrial-level planning and operations.
  This project served as an excellent platform to enhance our knowledge and explore various aspects of the subject in depth.
  We extend our sincere gratitude to Professor Sachin Mandavgane for assigning us this engaging topic and for his continuous guidance and support.
  We are thankful to our peers for their constructive feedback and valuable inputs throughout the project.
  Lastly, we express our heartfelt thanks to our parents for their subtle yet significant contributions, encouraging and supporting us during the project design process.
ACKNOWLEDGEMENT

## Slide 4
CONTENT
01
INTRODUCTION
  STRUCTURE
  USES
  PROPERTIES-PHYSICAL AND CHEMICAL
02
03
04
05
06
07
08
REACTIONS
  REACTION MECHANISM
  REACTION TYPE
PROCESS DESCRIPTION AND CALCULATIONS
  PROCESS FLOW DIAGRAM
  DESCRIPTION OF UNIT PROCESS
MATERIAL BALANCE AND ENERGY BALANCE
  AGITATOR
  DISTILLATION COLUMN
PLANT DESIGN AND CALCULATI0N
  STORAGE TANK
  CSTR DESIGN
  DISTILLATION COLUMN
  GRAVITY DECANTER
  PIPES AND PUMPS
SAFETY
PLANT LAYOUT
BIBLIOGRAPHY

## Slide 5
  List of tables
  List of Figures
  Chemical to be manufactured(Acetone)
  Physical and Chemical Properties
  Chemical Reaction
  Process Flow Diagram
  Process Description.
  Material Balance Calculations
  Energy balance calculation
  Section wise design calculation
1.Storage tank
2.Piping
3.Pumps
4.Reactors
  Another equipment based on the Process flow diagram
  Results in a tabular form
  Sr No | Tank No | Chemical to store | Capacity | Dimensions | Thickness |
  Safety
  Plant Layout
  Bibliography
INDEX

## Slide 6
1.INTRODUCTION
What is Acetone?
Acetone (propanone) is the simplest and smallest ketone. It is a colorless, volatile liquid with a characteristic sweet odour.
Importance:
  Widely used as an organic solvent in various industries.
  Plays a significant role in chemical synthesis.
Molecular Formula: C₃H₆O
Other Names: Propanone, Dimethyl Ketone

## Slide 7
1.INTRODUCTION
1.1 Structure
  Molecular Formula: C₃H₆O
  Molecular Geometry: Trigonal planar around the carbonyl carbon.
  Structure Diagram:
  Functional Group: Ketone (-C=O)
  Bond Angles: Approximately 120° around the carbonyl group.

## Slide 8
1.INTRODUCTION
1.2 Uses
  Industrial Applications:
    Solvent for paints, varnishes, and adhesives.
    Used in the production of plastics, fibers, and pharmaceuticals.
  Laboratory Uses:
    Common solvent for cleaning glassware and equipment.
    Used as an extraction agent in organic synthesis.
  Consumer Applications:
    Main ingredient in nail polish removers.
    Degreaser for household and industrial cleaning.

## Slide 9
1.INTRODUCTION
1.3 Physical properties
  State: Liquid
  Color: Colorless
  Odor: Sweet, pungent
  Melting Point: −94.7 °C
  Boiling Point: 56.05 °C
  Density: 0.7845 g/cm³
  Solubility: Miscible with water, alcohol, and most organic solvents.
  Vapor Pressure: 231 mmHg at 25 °C
1.4 Chemical properties
  Reactivity:
Combines with hydrogen to form isopropanol.
Oxidizes to acetic acid in the presence of oxidizing agents.
  Stability:
Stable under normal conditions.
Highly flammable; vapors form explosive mixtures with air.
  Combustion Reaction:
C₃H₆O + 4O₂ → 3CO₂ + 3H₂O

## Slide 10
2.REACTION
2.1 REACTION MECHANISM
Benzene and isopropylene react to form cumene:
Cumene is oxidized to produce cumene hydroperoxide and then hydrolysed to form phenol and acetone

## Slide 11
2.REACTION
2.2 REACTION TYPE
  The reaction of benzene with propylene to form cumene (isopropylbenzene) is an electrophilic aromatic substitution.
  In this reaction, propylene is first activated by a Lewis acid catalyst (commonly aluminum chloride or a similar acid) to generate a carbocation intermediate.
  This electrophilic species reacts with benzene, substituting one of its hydrogen atoms to form cumene.
  The hydrolysis of cumene to produce phenol and acetone is known as the cumene process. This involves the oxidation of cumene with oxygen (air) to form cumene hydroperoxide, followed by acidic cleavage. The cleavage yields acetone as our desired product.

## Slide 12
3. PROCESS DESCRIPTION
The industrial production of acetone (500 TPD) is integrated into the cumene process, where acetone and phenol are co-produced. Benzene undergoes alkylation with propylene in the presence of a Lewis acid catalyst to form cumene, with a benzene conversion efficiency of 98%. Cumene is oxidized with air at controlled temperatures (90–110°C) to produce cumene hydroperoxide (CHP), achieving a 94% single-pass conversion. The CHP is then cleaved under acidic conditions (50–70°C), yielding phenol and acetone. The reaction mixture is separated and purified through fractional distillation to recover high-purity acetone. Efficiency is maintained by recycling unreacted benzene and cumene, optimizing energy via heat integration, and ensuring environmental compliance.

## Slide 13
PLANT LAYOUT

## Slide 14
PROCESS FLOW DIAGRAM

## Slide 15
3.2 DESCRIPTION OF UNIT PROCESSES
3.2.1 DESCRIPTION OF STORAGE TANKS
BENZENE
  Molecular Mass :58 g/mol
  Density: 0.784 g/ml
  Melting Point: 178 K
  Boiling Point: 329 K
  Storage Tank Material: STAINLESS STEEL
ACETONE
  Molecular Mass :78.11 g/mol
  Density:0.874 g/ml
  Melting Point: 278 K
  Boiling Point: 353 K
  Storage Tank Material: STAINLESS STEEL
BENZENE
BENZENE
  Molecular Mass : 42 g/mol
  Density: 1.036 g/ml
  Melting Point: 87.95K
  Boiling Point: 225 K
  Storage Tank Material: STAINLESS STEEL
BENZENE
  Molecular Mass :120.1 g/mol
  Density: 0.864 g/ml
  Melting Point: 177 K
  Boiling Point: 425 K
  Storage Tank Material: STAINLESS STEEL
CUMENE
PROPYLENE

## Slide 16
Material Balance Calculations
  Acetone produced = 500 tonnes/day = 5x105 kg/day = 8620.57 kmol per day
  Phenol produced = 97 tonnes/day = 8620.69 kmol/day = 810.34 tones/day =810344.9 kg/day
  Conversion percentage of cumene hydroperoxide to phenol = 90%
  Moles of cumene hydroperoxide = 8620.69/0.94 = 9170.25 kmol/day
  Conversion percentage of cumene to cumene hyperoxide = 90%
  Moles of cumene inlet= 22927.38 kmol/day
  Conversion percentage of benzene to cumene = 98%
  Moles of benzene inlet = 22927.38/0.98 = 23395.29 kmol/day

## Slide 21
Basis: For 1 day of operation
Equation for Energy Balance:
Q = ΔHout – ΔHin + r ΔHf
Where:
Q = Heat absorbed or released in the reactor
ΔHout = Change in enthalpy in the system out
ΔHin = Change in enthalpy in the system in
r = Rate of reaction, ΔHf = Heat of formation at 298.15 K
ENERGY BALANCE CALCULATIONS

## Slide 22
Enthalpy Change for Components:
Enthalpy change formula
𝑡2
ΔH=∫
𝐶𝑝.𝑑𝑡
𝑡1
ΔH = A(T2 - T1) + (B/2)(T2
2
3
2 - T1) + (C/2)(T2 – T
Parameters:
•
•
T1 = Reference Temperature (298.15 K)
T2 = Input/Output Temperature
) + (D/4)(T
– T
)
3
1
4
2
4
1

## Slide 23
•
• • •
Examples of Components:
- Benzene: A=-0.206, B=29.064, C=-13.301
- Propylene: A=1.637, B=22.706, C=-6.915
- Cumene: A=0.189, B=0.538, C=-0.387, D=120.5x10^-7

## Slide 24
Enthalpy Changes for inflow: T2=210℃ =483.15°K T1=298.15°K ΔHin=0
Enthalpy change for outflow:
T2=210℃ =483.15°K
T1=298.15°K

## Slide 25
• For Benzene:
ΔH = (-0.206)(483.15 - 298.15) + (0.039064)(483.15² - 298.15²)/2 + (-0.000013301)(483.15³ - 298.15³)/3
Result: ΔH = 2.402 kJ/mol
• For Propylene:
ΔH = (1.637)(483.15 - 298.15) + (0.022706)(483.15² - 298.15²)/2
+ (-0.000006915)(483.15³ - 298.15³)/3
Result: ΔH = 1.7449 kJ/mol

## Slide 26
• For Cumene:
ΔH = (0.139)(483.15 - 298.15) + (0.000538)(483.15² - 298.15²)/2
+ (-0.000000397)(483.15³ - 298.15³)/3 + (120.5 × 10⁻12)(483.15⁴ - 298.15⁴)/4
Result: ΔH = 0.546 kJ/mol

## Slide 27
•For overall enthalpy at inflow:
ΔHin=0
For overall enthalpy at outflow:
ΔHout = 2.402 × 467.91 × 10³ + 1.7249 × 467.91 × 10³
+ 0.546 × 22927.38 × 10³
Result: ΔHout= 14458.732 × 10³ kJ/day.
• Heat of Formation:
= (-411 × 22927.38 × 10³) - (-49.08 × 467.91 × 10³

## Slide 28
+ 19.710 × 467.91 × 10³ - 28.5 × 467.91 × 10³)
Result: -961167.5 × 10³ kJ/day.
• Overall=-946708.77 × 10³ kJ/day (Exothermic).

## Slide 29
•
Compounds cummene Oxygen Cumene hydroperoxide
Reaction:
0.1392 0.0291 1.345*105
10^3B 0.5376 0.01158 3.8060*105
10^6C
-0.3979
-0.00671
-
10^-5D 120.5*10
1.311*10 -
17
-12
A

## Slide 30
Enthapy change for inflow:
•
Temperature Details:
(T₁ = 298.15 K T₂ = 383.15 K = 110°C)
For Cumene:
•
ΔH = (139.2×10⁻³)(383.15 - 298.15) + (53.76×10⁻⁵)(383.15² - 298.15²)/2+ (-39.79×10⁻⁸)(383.15³ - 298.15³)/3 + (120.5×10⁻¹²)(383.15⁴ - 298.15⁴)/4
Result:ΔH = 23.864 kJ/mol
•

## Slide 31
•
For Oxygen:
ΔH = (29.1×10⁻³)(383.15 - 298.15) + (1.158×10⁻⁵)(383.15² - 298.15²)/2 + (- 0.606×10⁻²)(383.15³ - 298.15³)/3 + (1.211×10⁻¹²)(383.15⁴ - 298.15⁴)/4
•
Result:
ΔH = 2.753 kJ/mol

## Slide 32
Enthapy change for outflow:
•
• Components analyzed:
  Cumene Hydroperoxide
  Cumene
  Oxygen
Temperature Details:
((T₁ = 298.15 K
T₂ = 383.15 K = 110°C)

## Slide 33
• Detailed Results: Cumene Hydroperoxide & Cumene
• Cumene Hydroperoxide:
ΔH = (1.345 × 10⁵)(388.15 - 298.15) + (3.806 × 10²)(388.15² - 298.15²)/2 Result: ΔH = 23.859 kJ/mol
• Cumene:
ΔH = (139.2 × 10⁻³)(388.15 - 298.15) + (58.76 × 10⁻⁵)(388.15² - 298.15²)/2 + (-39.79 × 10⁻⁸)(388.15³ - 298.15³)/3 + (120.5 × 10⁻¹²)(388.15⁴ - 298.15⁴)/4
  Result:
ΔH = 25.336 kJ/mol

## Slide 34
• Oxygen:
ΔH = (29.1 × 10⁻³)(388.15 - 298.15) + (1.158 × 10⁻⁵)(388.15² - 298.15²)/2+ (-0.6076 × 10⁻⁸)(388.15³ - 298.15³)/3 + (1.311 × 10⁻¹²)(388.15⁴ - 298.15⁴)/4
  Result:
ΔH = 2.917 kJ/mol

## Slide 35
Overview of inflow, outflow, and heat of formation
Enthalpy Calculations (Inflow and Outflow)
:
Overall Enthalpy for Inflow:
23.864 × 22927.38 × 10³ + 2.75 × 303.2 × 9170.95 × 10³
= 572386.9 × 10³ kJ/day
Overall Enthalpy for Outflow:
23.859 × 9170.95 × 10³ + 25.336 × 13756.43 × 10³ + 2.947 × 10³
= 567342.607 kJ/day
• • • • • •

## Slide 36
Heat of Formation and Overall Results:
•
For Heat of Formation: (-149.67 × 9170.95 × 10³) - (-41.1 × 22927.38*103)
= -1372616.09 × 10³ + 942315.318 × 10³ = -430300.772 kJ/day
Overall = (567342.607 - 572386.9- 430300.772) × 10³
= -435345.065 × 10³ kJ/day (Exothermic)

## Slide 37
Cumene HydroPeroxide
Phenol
Acetone
Compounds
A
10^3 B
10^6 C
10^ -5 D
1.345*10^5
-158.755
10.51
0.02199
4.964* 10^3
3.806* 10^5
-
-
-
1.57* 10^-15
-2.442*10^3
-0.7931
  Reaction:

## Slide 38
ΔH = (1 * 345 * 10 ^ 5)(403 * 15 - 298 * 15) + (- 758 - 3 * 806 * 10 ^ 2)(403 * 15 ^ 2 - 298 * 15 ^ 2) / 2
  Enthalpy change for inflow:
  For Cumene HydroPeroxide:
T₂=403.15 K
T = 298.15K
= 42148.552 kJ/mol

## Slide 39
= -1200 98.602 J/mol = -120-09 kJ/mol
  Enthalpy change for outflow:
T₁ = 298.15 K
T₂ = 383.15 K
  For Cumene HydroPeroxide:
ΔH= (1.345x105) (423.15-298.15)+(3.306*10 ^ 2)(423.15 ^ 2 - 293.15 ^ 2) / 2
=51128.348 J/mol = 51.128 kJ/mol
  For Phenol:
ΔH=(- 158.755)(423.15 - 298.15) +(4 ..964)(423.15 ^ 2 - 298.15 ^ 2) /2 +(-2.442x10^-3) (423.15^3-298.15^3)/3
=-1200 98.602 J/mol = -120.09 kJ/mol

## Slide 40
[(-96*4*86 20 * 69 + (- 247.48) * 8620 * 69 ]-
[(- 149 * 67) * 9170 * 95] ]* sqrt 2 ^ 3 =-1591866-791×1KJ/day
  For Acetone:
ΔH= (10.5(1))(423.15 - 298.15) +(0.02199×10-3) (423.15^2-298.15^2)/2+
(-0.7931x10^-6) (423.15^3-298.15^3)/3+ (1.57*10 ^ - 10)(423 .5 ^ 4 - 298.15 ^ 4) / 4
= 1302.665 KJ/mol

## Slide 41
STORAGE TANK CALCULATION
1)ACETONE : V= (5*105)/784 = 637.5 M3/DAY
FOR 2 MONTHS = 631-75 M^3/DAY*60 DAYS
=38265 M
CONSIDERING BUFFER FOR I MOUTH AND STORAGE OF WATE WE ARE MAKING I STORAGE TANKS OF
V= 38765/4 = 9566.25
MATERIAL: STAINLESS STEEL.
DIMENSIONS OF TANK: (H/D)= 1.5
=PI*(R^2)*H = 9566-25 =10811.69
=15 JID3 = 9566-25 =D-9-33 Ш
=H=9.33X1.5 = 18.995 1
CONSIDERING SAFETY FACTOR = 13.995×1.3 = 18.194M = H
ACETONE :
V=( 5x10^5 )/(784)=637.75m^3/day
For 2 months = 637.75 m³/day *60 days
= 38265 m3
Considering buffer for one month and storage.
We are making four storage tanks of V= 38265/4 = 9565.25 m^3
Material==>> Stainless steel.
Dimensions of tank: (H/D)= 1.5
=> πr^2 H = 9566.25
=>(1.5/4)*πD^3 = 9566.25
D=9.33 m
H=9.33*1.5 = 13.995 m
Considering safety factor = 13.995*1.3 = 18.194 m = H
Thickness = 2.5 mm

## Slide 42
PHENOL:
V= 810344.9/1058 = 765.92 m^3/day
For 2 months = 45955.29 m^3
For 1 tank = 45955.291/4=11488.82 m^3
Material: Stainless Steel
Dimensions of tank: (H/D) = 1.5
=> π*r^2*H= 11488.82
=>(1.5/4) *π*D^3=11488.82
=> D^3=29752.01.
=>D=21.36 m
H=21.36 * 1.5 = 32.05 m
Considering safety factor= 32.05*1.3= 41.66m = H

## Slide 43
CUMENE:
V = 2751285.6/862 = 3191.75 m^3/day
For 2 months = 191504.8 m^3
For 1 tank = 191504.8/4 =47876.2 m^3
Material: Stainless Steel
Dimensions of tank: (H/D) = 1.5
π*r^2*H=47876.2
(1.5/4)*π*D^3=47876.2
D^3=40638.6m^3
D=34.38 m
H=34-38×1.5=51.57 m
Considering safety factor= 51.5.7*1.3 = 67.044 m=H
Thickness: 36 mm

## Slide 44
BENZENE:
V=1788335.64/876 = 2041.48 m^3/day
For 2 weeks=28580.72 m^3
For 1 tauk = 28580.72/4 = 7145.18 m^3
Material: Stainless steel
Dimensions of tank (H/D)=1.5
π*r^2*H=7145.18 m^3
(1.5)/4*π*D^3=7145.18
D=18.24 m
H=27.36 m
Considering safety factor:
21*1.3=37.57 m=H
Thickness = 10.77 mm
-

## Slide 45
Cumene Hydroperoxide:
Cumene volume = 121328 m^3/day.
6 days volume= 72796.93 m^3day.
Divided in 4 tanks,
H/D =1.5
(1.5)*π*D^3/4=18199.23 m^3
D=24 m
H=37.36 m
Considering safety factor:
Hsafe = 37.36 *13
=48.573 m

## Slide 46
PROPYLENE:
V=982602.18/480=2047.087 m^3/day
For 2 weeks =28659.2302 m^3/day
Considering 4 tanks:
For 1 tank = 28659.2302/4=7164.807
Material: Stainless Steel
Dimensions of tank (H/D) = 1.5
(1.5/4)*π*D^3=7164.807
D= 18.25 m
H=1.5*18.25=27.38 m
Considering safety factor:
1.3*27.38=35.594 m
Thickness = 5.65 mm

## Slide 47
STORAGE TANK | DIAMETER(M) | HEIGHT WITH 30% SAFETY FACTOR(m) | Thickness(in mm)
PROPYELENE(x4) | 18.25 | 35.5 | 5.65
BENZENE(x4) | 18.24 | 37.57 | 10.77
CUMENE(x4) | 34.3 | 67.044 | 36
CUMENE HYDROPEROXIDE | 24 | 37.57 | -
ACETONE(x4) | 9.3 | 18.1 | 2.5
TABLE OF STORAGE TANK DIMENSIONS

## Slide 48
Pipe Section : 1-(Propylene to CSTR 1)
  Assuming Velocity = 2m/sec
  Density of Propylene ,ρ=480 kg/m3
  Viscosity of Propylene , μ=5.02 x 10−3 Pa.s
Volumetric flow rate ,Q =Mass flow rate(m)
Density
  Mass flow rate = 518570.22 kg/day =6.0019 Kg/sec
Q =6.0019 kg/sec
480 kg/m3
=0.0125 m3/sec
Volumetric flow rate ,Q =Area (a) x Velocity (v)
CSTR-1

## Slide 49
  Area ,a = 0.0125
2
= 0.00625 m2
  D=0.08921 m = 89.21 mm
Nominal Pipe Size Selection
From the Asme B36 10 standard , the closest pipe size is NPS 3 inches which has an outside diameter (D) of 88.9 mm .This is very close to our calculated diameter
Wall thickness ,t = PD
2σJ - p
  P= 1.5 Mpa (design pressure)

## Slide 50
  Outside Diameter ,D = 88.9 mm
  Joint efficiency ,σ=138Mpa
t = 1.5 x 0.088
2 x 138 -1.5
t=0.572 mm
Adding a corrosion allowance of 1.5 mm(typical carbon steel) for safety compilance
t=0.572+1.5=2.072 mm

## Slide 51
Selecting Pipe Schedule
  Schedule 40 has a thickness of 3.91 mm (greater than our calculated)
  Nominal pipe size 3 schedule 40 pipe is suitable for this applicaton
Pressure drop across pipeline
  ε =0.015 mm
  The length of pipe line = 34.6 m
  Now,finding the value of head loss,
  P/g=(4fL/D + K)x V^2/2g
  4fL/D=34.13m
  K=Minor losses and elbow losses=14.25
  P/g=48.21x4/2x9.81=9.91m
  Pressure head loss=9.91m
  Pressure loss in pipe=164.38Kpa

## Slide 52
PIPE SECTION-3:CSTR-1 TO CUMENE STORAGE TANK
Assuming velocity equals to 2m/s
  Density of cumene at 110c=862kg/m^3
  Viscosity of cumene = 0.79x10^-Volumetric flow rate =2751285.6kg/day=31.84kg/s
  Q=31.84/862=0.0369m^3/s
  Q=AxV
  A=0.0369/2=0.0184=
  3.14xD^2=4x0.01874
  D=0.132=5.2inches
  For 40 schedule pipe and NPS 5.5inches the thickness of pipe is 0.258mm
  Length os pipe section is 67.03+5+1+1=74.03
  3 Elbows are considered here
  e/D=0.000046/0.13=0.0003538
  Re=283696.2 flow is turbulent

## Slide 53
  Now,finding the value of head loss,
  P/g=(4fL/D + K)x V^2/2g
  4fL/D=4x0.017x74.03/0.132=38.136
  Minor losses=14.5
  p/g=(38.136+14.5)x4/(2x9.81)=11.46m
  Pressure head loss=96.8Kpa
  frictional head loss=7.74m

## Slide 54
  Weight of cumene hydroperoxide=1310344.88kg/day=15.16kg/s
  Density of cumene hydroperoxide=1020kg/m^3
  Viscosity of cumene hydroperoxide=0.077mPa
  Volumetric flowrate=15.16/1020=0.0148m^3/s
  Q=A x V
  0.0148/2=0.00743=A
  0.00743=3.14xD^2/4
  D=0.097m=3.8 inches
  For 40 schedule pipe of NPS 3.8' the thickness is 0.237mm
  Length of pipe section=48.57+10+1+1=60.57
  Reynolds number=(1020x2x0.097)/(0.077x10^-3)
  R=2569870 the flow is turbulent
  E/D=0.000046/0.097=0.000474
PIPE CALCULTIONS
SECTION 4:FROM CUMENE HYDROPEROXIDE TO CSTR-2
CSTR 2

## Slide 55
  From referring moody chart and finding value of frictional factor for Re and e/D
  The value of frictional factor is 0.0136
  Now,finding the value of head loss,
  P/g=(4fL/D + K)x V^2/2g
  4fL/D=33.96
  K=Minor losses and elbow losses=14.25
  P/g=48.21x4/2x9.81=9.83m
  Pressure head loss=9.83m
  Pressure loss in pipe=98.37Kpa

## Slide 56
PIPE SECTION | PIPE DIAMETER (inches) | PIPE LENGTH (m) | Z | frictional factor(f) | PRESSURE HEAD (m) | FRICTOINAL HEAD (m)
FROM PROPEYLENE TANK TO CSTR-1 | 3 | 34.4 | 22.4 | 0.022 | 9.91 | 
FROM BENZENE TANK TO CSTR-1 | 4.8 | 34.4 | 22.4 | 0.0174 | 29.5 | 6.85
FROM CSTR-1 TO CUMENE TANK | 5.2 | 74.03 | 64.03 | 0.017 | 11.46 | 7.74
FROM CUMENE HYDROPEROXIDE COLUMN TO CSTR-2 | 3.8 | 60.57 | 48.57 | 0.0136 | 9.83 | 
TABLE OF PIPE CALCULATION

## Slide 57
PUMP CALCULATIONS
Section 1 :
From Propylene storage tank to CSTR
Pipe: diameter = 0.0892 m
Volumetric flow Rate (Q) = velocity*area
=2 */4
=0.0125 m3/s
Material of Pipe: Stainless steel pipe
Length of pipe= 34.6 m
∆Z for pipe = 10 m
Pipe has three 90⁰ Elbows and 2 valves
Kf for 900 Elbows = 0.75
Kf for valve = 6
= (30.75 + 62) = 14.25
We have friction factor f = 0.02

## Slide 58
= (50000/480*9.81) + 10 - 9.3 - (4/2*9.81) = 9.746m
Power required
= m * g* Hp
= Q* *g*Hp
= 0.0125 * 480 * 9.81 * 22.46
= 1.321 kW
Considering pump to be 80 % efficient
Power required = 2.21 Hp

## Slide 59
Pump calculations and results

## Slide 60
Kirloskar Pump performance curves

## Slide 62
_-CSTR Calculations-_

## Slide 64
Safety Measures for Propylene Storage Tanks
Storing propylene requires strict safety protocols due to its flammable and pressurized nature. Key measures include:
1. Material Selection: Use corrosion-resistant stainless steel with high pressure tolerance.
2. Pressure Relief Systems: Install calibrated relief valves and emergency vents to prevent overpressure.
3. Fire Prevention: Use gas detectors, explosion-proof equipment, and fire suppression systems.
4. Temperature Control: Monitor and regulate tank temperature to avoid pressure buildup.
5. Emergency Systems: Provide automatic shutdown systems and accessible manual controls.
6. Spill Containment: Build bund walls or secondary barriers to contain leaks.
7. Inspections and Training: Conduct regular inspections and train staff on safety and emergency procedures.
8. Regulatory Compliance: Adhere to standards like API 620 and ASME Section VIII.
These measures ensure safe handling, environmental protection, and operational reliability.

## Slide 65
BIBLIOGRAPHY:
1.Fluid Mechanics for Chemical Engineers by Noel-de-Nevers.
2Analysis, Synthesis, and Design of Chemical processes by Richard turton
3.https://pubchem.ncbi.nlm.nih.gov/compound/Acetone
4.https://www.researchgate.net/publication/368661065_Acetone_Production_Process.
5.https://en.wikipedia.org/wiki/Acetone.

## Slide 66
THANK YOU